## Slide 1: I2C parts and registers
Power Monitor (I2C addr = 0x40):
  Power on config is a good starting point so don’t alter 16 bit config reg (00h) can later change to triggered and power-down in between measurements to reduce power
  Read Reg 01h: Current
  Read Reg 02h: Voltage
ADC (I2C addr = 0x1D)
  Config reg 0Bh default (of all 0’s) is perfect
  Conv rate reg 07h default (of all 0 - read all regs once then low power) is perfect
  Reg 00h set to 08h or 00h ?? (to reset conversion)
  Reg 00h set to 09h or 01h ?? (to start conversion)
  Reg 09h write 01h (can be anything) to perform a one shot single conversion
  Wait 1 second
  Read Reg 20h through 27h and expect 16 bits of data (for in0 to in7) Vinx = 12bit digital * 2.56/2^12

## Slide 2: I2C Power Board
I2C input pins on the DSP Power board: SCL = J6 & J5.8 SDA = J6 & J5.7
Chips:
  Power monitor INA260AIPW (I2C addr = 0x40)
  8 channel 12bit ADC ADC128D818CIMPX (I2C addr = 0x1D)
    Ch0 Bank1_current(3.74K) VN5T006ASP ( 1A = 0.37V)
    Ch1 Bank2_current (3.74K)
    Ch2 Aux_current (3.74K)
    Ch3 1/6 Bank1 Voltage
    Ch4 1/6 Bank2 Voltage
    Ch5 1/6 Aux Voltage
    Ch6 3.3v Voltage
    Ch7 5v Voltage